## Slide 1
AutoSSD: an Autonomic SSD Architecture
张翔
10/30/2018

## Slide 2
Outline
Background and Motivation
Overview of AutoSSD
AutoSSD Architecture
Evaluation Methodology and Modeling
Experiment Results
Conclusion

## Slide 3
Background and Motivation
Flash translation layer (FTL)--internal management schemes
  Mandating a mapping table between the logical and the physical address space.
  Garbage collection (GC)
The uncoordinated use of resources by competing tasks in FTL makes it difficult to guarantee predictable performance.
  AutoSSD, an autonomic SSD architecture that self-manages FTL tasks to maintain a high-level of QoS performance.

## Slide 4
Overview of AutoSSD
Each FTL task is given a virtualized view of the flash memory subsystem
Each task is allocated a share that represents the amount of progress it can make,and a simple yet effective scheduling scheme enforces resource arbitration according to the allotted shares.
The shares are dynamically and automatically adjusted through feedback control by monitoring key system states and reacting to their changes.

## Slide 5
AutoSSD Architecture
Share controller
  Monitor key system states and determines the appropriate share for each FTL task

## Slide 6
AutoSSD Architecture
Virtualization of the Flash Memory Subsystem
  Each task to be independent of others
  Each FTL task is given a pair of request and response queues
  This virtualization not only effectively frees each task from having to worry about others, but also makes it easy to add a new FTL task to address any future flash memory quirks.

## Slide 7
AutoSSD Architecture
Scheduling subsystem
  Interface with each FTL task and arbitrates the resources of the flash memory subsystem
  Needs to be efficient with low overhead
  Debit(the number of outstanding requests for a task) scheduling
    Tracks and limits(proportional to the share) the number of outstanding requests per task across all resources
    Skewed randomness favoring a task with a smaller debit

## Slide 8
AutoSSD Architecture
The share controller
  Determine the appropriate share for the scheduling subsystem by observing key system states:
    number of free blocks -- response time
    maximum read count for a block -- data loss
  SA[t] is the share for task A at time t,SA[t−1] is the previous share for task A,PA and IA are two nonnegative coefficients,eA[t] is the error value for task A at time t； targetfreeblk[t] is the number of target free blocks,numfreeblk[t] is the number of free blocks.

## Slide 9
Evaluation Methodology and Modeling
Mapping: 4KB granularity，LRU（Least Recently Used），128MB mapping table
Host request handling：Mapping table lookup delay 0.5µs~1µs,flash memory request generation delay for the host task 1µs~2µs
Garbage collection：threshold values for GC activation and deactivation are set to 128 and 256 free blocks，request generation delay 1µs~3µs

## Slide 10
Evaluation Methodology and Modeling
Workload
  synthetic workloads and real-world I/O traces from Microsoft production servers

## Slide 11
Experiment Results
Micro-benchmark Results
  b:100K I/Os per second (IOPS)
  c:20K IOPS with a 1-to-9 read/write ratio

## Slide 12
Experiment Results
I/O Trace Results
  Vanilla:without virtualization and coordination,a single pair of request/response queue
  RAIN:use parity to reconstruct data when chip is blocked by background tasks,fixed priority scheduling,host requests having the highest priority
  QoSFC:weighted fair queueing (WFQ)

## Slide 13
Experiment Results
I/O Trace Results

## Slide 14
Experiment Results
I/O Trace Results

## Slide 15
Experiment Results
I/O Trace Results at Higher Request Intensity -- request dispatch times are reduced in half
  AutoSSD reduces the average response time by up to 24.6% under MSN-BEFS (by 4.9% on average),the 3 nines QoS by up to 70.6% under MSN-CFS (by 48.6% on average).and the 6 nines QoS by up to 55.3% under MSN-CFS (by 33.2% on average).

## Slide 16
Experiment Results
I/O Trace Results at Higher Request Intensity -- request dispatch times are reduced in half

## Slide 17
Conclusion
An autonomic SSD architecture that self-manages concurrent FTL tasks in the flash storage
  In effect, AutoSSD reduces the average response time by up to 18.0%, the 3 nines (99.9%) QoS by up to 67.2%, and the 6 nines (99.9999%) QoS by up to 76.6% for QoS-sensitive small reads

## Slide 18
Thanks！